## Slide 1
Design of a Preliminary Family of Airfoils for High Reynolds Number Wind Turbine Applications
Cody Karcher*
California State University, Long Beach
David Maniaci, Chris Kelley, Alan Hsieh, and Nate deVelder
Sandia National Laboratories
Anurag Gupta
National Renewable Energy Laboratory
Sandia National Laboratories is a multimission laboratory managed and operated by National Technology and Engineering Solutions of Sandia LLC, a wholly owned subsidiary of Honeywell International Inc. for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
SAND2025-00716C

## Slide 2: Wind turbines have significantly increased in size over time
https://www.energy.gov/eere/articles/wind-turbines-bigger-better

## Slide 3: Some airfoils exist, but do not match the current need
Notes: FFA airfoils are designed for a much lower Re regime and sacrifice performance (similar with all airfoils)

## Slide 4: There are also access issues for many of the best airfoils
Not Open Source
(approximated from images in the literature)
Fully Open Source
Notes: FFA airfoils are designed for a much lower Re regime and sacrifice performance (similar with all airfoils)
S-series Airfoils had significant spar offsets, complicates spar integration
Remaining airfoils are not open source (although some are shared by request, such as DU airfoils)

## Slide 5: This increase in size has pushed us into new physics regimes
Design range FFA airfoils

## Slide 6: But these airfoils are not designed for this task…
Design range FFA airfoils

## Slide 7: IEA 22MW Reference Turbine uses the FFA Airfoils
Zahle et. al., Definition of the IEA Wind 22-Megawatt Offshore Reference Wind Turbine, 2024
Internal Structure
Outer Mold Line

## Slide 8
We need new airfoil options that are:
Open Source
Designed for modern applications
A reflection the state of airfoil design post 1990

## Slide 9
Today we are presenting preliminary results
We want input from the community!

## Slide 10: Design Approach

## Slide 11: Meetings with advisory committee yielded design requirements
Normalized Thickness | 21% | 24% | 27% | 30%
Design Lift Coefficient | 1.5 | 1.4 | 1.3 | 1.2
Angle of Attack | N/A | N/A | N/A | N/A
Reynolds Number | 12e6 | 13e6 | 16e6 | 18e6
Clean L/D | 200 | 190 | 185 | 180
Rough L/D | 110 | 110 | 105 | 100
Stall Margin | 4 deg | 4 deg | 4 deg | 4 deg
Pre-Stall Lift Coefficient Margin | 0.2 | 0.2 | 0.2 | 0.2
Change in CL due to Roughness | 0.15 | 0.14 | 0.13 | 0.12
CM Clean | N/A | N/A | N/A | N/A
CM Rough | N/A | N/A | N/A | N/A
LE Radius | 0.01 | 0.025 | 0.03 | 0.04
Flap Stiffness (Ixx) | 0.00028 | 0.00041 | 0.00058 | 0.00080
Edge Stiffness (Iyy) | 0.00494 | 0.00561 | 0.00633 | 0.00706
Torsion Stiffness (Izz) | 0.00522 | 0.00602 | 0.00691 | 0.00786
Area | 0.11478 | 0.13051 | 0.14661 | 0.16290

## Slide 12: Specifically seeking guidance on Lift Coefficient…
Normalized Thickness | 21% | 24% | 27% | 30%
Design Lift Coefficient | 1.5 | 1.4 | 1.3 | 1.2
Angle of Attack | N/A | N/A | N/A | N/A
Reynolds Number | 12e6 | 13e6 | 16e6 | 18e6
Clean L/D | 200 | 190 | 185 | 180
Rough L/D | 110 | 110 | 105 | 100
Stall Margin | 4 deg | 4 deg | 4 deg | 4 deg
Pre-Stall Lift Coefficient Margin | 0.2 | 0.2 | 0.2 | 0.2
Change in CL due to Roughness | 0.15 | 0.14 | 0.13 | 0.12
CM Clean | N/A | N/A | N/A | N/A
CM Rough | N/A | N/A | N/A | N/A
LE Radius | 0.01 | 0.025 | 0.03 | 0.04
Flap Stiffness (Ixx) | 0.00028 | 0.00041 | 0.00058 | 0.00080
Edge Stiffness (Iyy) | 0.00494 | 0.00561 | 0.00633 | 0.00706
Torsion Stiffness (Izz) | 0.00522 | 0.00602 | 0.00691 | 0.00786
Area | 0.11478 | 0.13051 | 0.14661 | 0.16290

## Slide 13: …along with Moment Coefficient
Normalized Thickness | 21% | 24% | 27% | 30%
Design Lift Coefficient | 1.5 | 1.4 | 1.3 | 1.2
Angle of Attack | N/A | N/A | N/A | N/A
Reynolds Number | 12e6 | 13e6 | 16e6 | 18e6
Clean L/D | 200 | 190 | 185 | 180
Rough L/D | 110 | 110 | 105 | 100
Stall Margin | 4 deg | 4 deg | 4 deg | 4 deg
Pre-Stall Lift Coefficient Margin | 0.2 | 0.2 | 0.2 | 0.2
Change in CL due to Roughness | 0.15 | 0.14 | 0.13 | 0.12
CM Clean | N/A | N/A | N/A | N/A
CM Rough | N/A | N/A | N/A | N/A
LE Radius | 0.01 | 0.025 | 0.03 | 0.04
Flap Stiffness (Ixx) | 0.00028 | 0.00041 | 0.00058 | 0.00080
Edge Stiffness (Iyy) | 0.00494 | 0.00561 | 0.00633 | 0.00706
Torsion Stiffness (Izz) | 0.00522 | 0.00602 | 0.00691 | 0.00786
Area | 0.11478 | 0.13051 | 0.14661 | 0.16290

## Slide 14: Design process uses XFOIL with RFOIL for validation
Write Objective Function using XFOIL
Run Genetic Algorithm on Sandia HPC
Select High Performing Candidates from
GA Results
Modify Airfoils to Match Design Intent
(As Needed)
Validate XFOIL Data with RFOIL for Final Designs
Report Final Performance Metrics

## Slide 15: Does XFOIL capture the design space to the extent we need?
Run Genetic Algorithm on Sandia HPC
Select High Performing Candidates from
GA Results
Modify Airfoils to Match Design Intent
(As Needed)
Validate XFOIL Data with RFOIL for Final Designs
Report Final Performance Metrics
Write Objective Function using XFOIL

## Slide 16: XFOIL untrustworthy in an absolute sense, but is OK for design
Pires et. al., Analysis of High Reynolds Numbers Effects on a Wind Turbine Airfoil Using 2D Wind Tunnel Test Data, 2016
Free

## Slide 17: How does the Genetic Algorithm Perform?
Select High Performing Candidates from
GA Results
Modify Airfoils to Match Design Intent
(As Needed)
Validate XFOIL Data with RFOIL for Final Designs
Report Final Performance Metrics
Write Objective Function using XFOIL
Run Genetic Algorithm on Sandia HPC

## Slide 18: Genetic Algorithm successfully identifies promising designs

## Slide 19: Hand adjustments are made as needed to improve designs

## Slide 20: Airfoils and Performance Results

## Slide 21: The Preliminary Airfoil Family
21%
24%
27%
30%

## Slide 22: 21% Airfoil

## Slide 23: 21% Airfoil

## Slide 24: 30% Airfoil

## Slide 25: 30% Airfoil

## Slide 26: Hand Modified airfoils perform well in design metrics (RFOIL)
Normalized Thickness | 21% | 24% | 27% | 30%
Design Lift Coefficient | 1.5 | 1.4 | 1.3 | 1.2
Reynolds Number | 12e6 | 13e6 | 16e6 | 18e6
Angle of Attack | 9.67 | 6.39 | 6.43 | 7.72
Clean L/D | 183.36 | 202.80 | 184.58 | 156.10
Rough L/D | 124.14 | 106.43 | 109.60 | 95.42
Stall Margin (degrees) | 3.80 | 4.09 | 5.98 | 5.66
Pre-Stall Lift Coefficient Margin | 0.39 | 0.62 | 0.75 | 0.81
Change in CL due to Roughness | 0.01 | 0.08 | 0.06 | 0.01
CM Clean | -0.081 | -0.131 | -0.118 | -0.087
CM Rough | -0.073 | -0.123 | -0.110 | -0.078
LE Radius | 0.02216 | 0.02881 | 0.04809 | 0.05086
Flap Stiffness (Ixx) | 0.00030 | 0.00043 | 0.00060 | 0.00085
Edge Stiffness (Iyy) | 0.00578 | 0.00637 | 0.00721 | 0.00867
Torsion Stiffness (Izz) | 0.00608 | 0.00680 | 0.00782 | 0.00952
Area | 0.12399 | 0.13782 | 0.15487 | 0.17749

## Slide 27: Recent Refinements

## Slide 28: Recent Refinements

## Slide 29: Next Steps

## Slide 30: Future tasks are refinement and application
Continue to refine the requirements, objective function
  Consider family together as a whole and spar layout
  Consider 3D aero effects
  Model full rotor performance
Incorporate community feedback
  Final versions of these airfoils are being considered as candidates for experimental testing

## Slide 31: Questions?
Cody Karcher
cody.karcher@csulb.edu
David Maniaci
dcmania@sandia.gov
Please send us your comments at:

## Slide 32: Backup

## Slide 33: Design Lift Coefficient
Initially selected to be CL=1.2 for the entire family
Later selected CL=1.5 at tip reducing to CL=1.2 at ~40% span to follow IEA 22MW reference turbine design conditions
Should occur in the linear region of the CL-Alpha curve
Design Choice
CD
CL
CL
⍺
1.2
⍺des
Notes: The design lift coefficient is a design choice, so we are looking for suggestions of the most appropriate range.

## Slide 34: Lift to Drag Ratio (L/D)
Should be maximized with a target of between 170 and 200
Desire a clear increase over DU/FFA/Riso series
Desire more robust performance than S-series (broader peak, less Re# dependance)
Design Target
XFOIL Data at 3 Million Re
Normalized Thickness | 15% | 18% | 21% | 24% | 27% | 30% | 33% | 36%
L/D Target | 200 | 200 | 200 | 190 | 185 | 180 | 175 | 170

## Slide 35: Stall Margin--Clean
Angle of attack difference between design CL and CL,max
Must exceed 3 degrees for robustness to real-world conditions
Design Requirement
CD
CL
CL
⍺
⍺des
⍺stall
Stall Margin

## Slide 36: Stall Margin--Rough
Same as clean, but modeled using Ncrit and transition location
Must exceed 3 degrees for robustness to real-world conditions
Design Requirement
CD
CL
CL
⍺
⍺des
⍺stall,rough
Rough Stall Margin

## Slide 37: Lift Coefficient Margin to Stall
Should be minimized to limit gust loading
Target a nominally small value of 0.2
Design Target
CD
CL
CL
⍺
CL,des
CL Margin
CL,stall

## Slide 38: Change in Lift Coefficient Due to Roughness
Measured as change in CL at the AoA of the clean design CL
Limit to a change of less than 10% from clean baseline
Design Requirement
CD
CL
CL
⍺
⍺des
ΔCL
Notes: Is 10% drop in lift too high at the AoA for design Cl?

## Slide 39: L/D Ratio in the Operating Region--Smooth
L/D curve should be reasonably flat in the desired operating region
Target within 15% of (L/D)des within +/-15% of ⍺des
CL / CD
Design Target
CL
⍺des
0.85 ⍺des
1.15 ⍺des
ΔL/D
ΔL/D

## Slide 40: L/D Ratio in the Operating Region--Rough
Same as before, but for rough airfoil
Target within 5% of (L/D)des within +/-15% of ⍺des
CL / CD
Design Target
CL
ΔL/D
ΔL/D
⍺des
0.85 ⍺des
1.15 ⍺des

## Slide 41: Post-Stall Behavior
Post-stall slope is a major factor in blade fatigue
Should be minimized, but will only be used as a final selection criteria
Human Selection
CD
CL
CL
⍺
⍺stall
dCL /d⍺
(dCL /d⍺)neg
3 deg
Notes: Proposal is to compute this slope over say 3 degrees rather than capturing the actual local slope.

## Slide 42
Structural Performance

## Slide 43: Solid Body Geometry Properties
Performed a study of solid area geometry properties of existing airfoils
  Ixx (Bending), Iyy (Edgewise), Izz (Torsion), and Area
Strong correlation and separation from non-turbine airfoils
Will implement lower bound of existing airfoils as a design constraint
Design Requirement
Require Ixx to be higher than bound
Notes: We plan to set a constraint to have structural performance no worse than any current wind turbine airfoil families.
Can consider including tradeoffs in improving aero. vs. structure performance in later iterations, likely future work.
ARE THERE OTHER SIMPLE METRICS we could/should use?

## Slide 44
Geometry Considerations

## Slide 45: Robustness to Finite Thickness Trailing Edges
Will be designing sharp since true TE gap cannot be known a priori
Target less than 1% change in all metrics on the following thicknesses:
Thickness targets increase for thicker inboard airfoils
TE Gap
Normalized Thickness | 15% | 18% | 21% | 24% | 27% | 30% | 33% | 36%
TE Gap | 2mm | 2mm | 2mm | 3mm | 3.5mm | 4mm | 4.5mm | 5mm
Design Requirement

## Slide 46: Leading Edge Radius
Small LE radius causes inconsistent and rapid separation
Limit to somewhere between the DU and S series airfoils
R=0.008
Design Requirement
Normalized Thickness | 15% | 18% | 21% | 24% | 27% | 30% | 33% | 36%
LE Radius | 0.007 | 0.008 | 0.01 | 0.025 | 0.03 | 0.04 | 0.06 | 0.08

## Slide 47: Trailing Edge Wedge Angle
Ensures manufacturability and structural integrity
Last 2% of chord must have a wedge angle of at least 10 degrees
10o
0.98
Design Requirement

## Slide 48: Maximum Thickness Location
S-series airfoils had significant spar offsets
Will constrain max thickness to occur at the same x/c in this work
Line connecting the two max thickness locations should not be slanted
Design Requirement
Notes: Will do lofting of airfoils on actual 3D blade model at each design iteration stage as a higher fidelity check.
Impacts structural performance.